## Slide 1
C-DAC ACTS, PUNE | PGCP-DESD PROJECT REPORT
Real-Time EV Battery
Management System
with Safety Protections
Dual STM32F407 Microcontrollers • CAN Bus Communication • ESP32 IoT Dashboard (MQTT)
PRESENTED BY
Dhanush Raja A.K. PRN: 260240130011
Priya Rajendra Kulkarni PRN: 260240130031
Nikita Mandar Bhawalkar PRN: 260240130007
Rituja Sunil Bedse PRN: 260240130037
Abhay Uddhavrao Akhade PRN: 260240130001
Guided by: Mr. Arvind Kumar

## Slide 2
INTRODUCTION
Why EV Battery Safety Matters
As EV adoption accelerates, the battery pack becomes the most critical and expensive component of the vehicle. Abnormal conditions — overheating, excessive current, over/under-voltage, or smoke — can degrade battery life and trigger thermal runaway or fire. Conventional monitoring systems often lack real-time fault detection, reliable inter-controller communication, and remote visibility.
PROBLEM STATEMENT
Conventional battery monitoring systems often lack real-time fault detection, reliable communication between embedded controllers, and remote monitoring — increasing risk to battery life and vehicle safety.
Overheating
Thermal runaway risk
Over-current
Reduced battery life
Over / Under-voltage
Cell degradation
Smoke generation
Fire hazard
Motivation: continuous monitoring enables early detection of unsafe conditions, prevents costly failures, and — with IoT integration — supports predictive maintenance from anywhere.
Real-Time EV Battery Management System with Safety Protections
2

## Slide 3
AIM & OBJECTIVES
Project Aim, Objectives & Scope
To design and implement a Real-Time EV Battery Monitoring and Safety Protection System using dual STM32F407 microcontrollers, CAN communication, and an MQTT-based IoT platform.
OBJECTIVES
1
Monitor battery voltage & current (INA219)
2
Measure battery temperature (NTC thermistor)
3
Detect smoke concentration (MQ135)
4
Reliable inter-controller CAN communication
5
Real-time fault detection for abnormal conditions
6
Automatic safety control — cooling fan & buzzer
7
Transmit data to ESP32 via UART
8
Publish battery data to MQTT IoT dashboard
SCOPE Battery parameter monitoring, real-time fault detection, and safety indication via dual STM32F407 nodes over CAN, with IoT visualization. Excludes: charging control, cell balancing, and advanced SOH prediction (future work).
Real-Time EV Battery Management System with Safety Protections
3

## Slide 4
SYSTEM DESIGN
Distributed System Architecture
Two STM32F407 nodes over CAN bus, bridged to an MQTT IoT dashboard via ESP32
SENSORS
INA219 (I²C)
NTC (ADC)
MQ135 (ADC)
›
STM1
Sensor Acquisition
Node
(validate, filter)
›
CAN BUS
SN65HVD230
Transceivers
(every 100 ms)
›
STM2
Monitoring &
Control Node
(SOC, faults)
›
ESP32
UART → Wi-Fi
MQTT Publish
›
DASHBOARD
Cloud Broker
IoT Dashboard
Sensor Acquisition Node (STM1)
Reads INA219, NTC & MQ135; validates & filters data; packs CAN frames every 100 ms.
Monitoring & Control Node (STM2)
Computes power & SOC; detects faults; drives fan/buzzer; forwards data via UART.
Real-Time EV Battery Management System with Safety Protections
4

## Slide 5
HARDWARE
Key Hardware Components
STM32F407VGT6
ARM Cortex-M4 @ 168 MHz, 1 MB Flash, dual-node controller for acquisition & control
ESP32-WROOM-32
Dual-core Wi-Fi/BLE module — bridges UART data to the MQTT broker
INA219
I²C voltage & current sensor; 12-bit ADC, up to 26 V bus voltage
NTC Thermistor
Voltage-divider temperature sensing for overheat detection
MQ135 Gas Sensor
Analog smoke/gas detection for early fire-risk warning
SN65HVD230
3.3 V CAN transceiver linking STM1 and STM2 over CANH/CANL
Real-Time EV Battery Management System with Safety Protections
5

## Slide 6
CONNECTIVITY
Communication Architecture
I²C
STM1 ↔ INA219
Digital voltage/current read-out from the sensor to the acquisition node.
CAN Bus
STM1 ↔ STM2
Robust, noise-immune automotive protocol; frames sent every 100 ms.
UART
STM2 ↔ ESP32
Simple two-wire serial hand-off of processed battery data & fault status.
MQTT / Wi-Fi
ESP32 ↔ Dashboard
Lightweight publish-subscribe protocol for real-time cloud visualization.
Real-Time EV Battery Management System with Safety Protections
6

## Slide 7
SAFETY LOGIC
Fault Detection & Safety Response
STM2 continuously evaluates battery health and triggers protective actions in real time
Under / Over-Voltage
→ Warning & fault flag raised
Over-Current
→ Buzzer activated
High Temperature
→ Cooling fan switched ON
Smoke Detected
→ Continuous buzzer alert
CAN Comm. Failure
→ Communication fault flagged
Sensor Fault
→ Reading invalidated & logged
Priority-based safety handling. A fault-priority mechanism ensures the most critical condition is handled first, and temperature hysteresis prevents frequent fan ON/OFF switching near the threshold.
Real-Time EV Battery Management System with Safety Protections
7

## Slide 8
IMPLEMENTATION
Software Implementation & Dev Tools
FIRMWARE FLOW
STM1
Init ADC/I²C/CAN → read & validate sensors → filter noise → pack & send CAN frame (100 ms)
STM2
Init CAN/UART → receive frame → compute Power/SOC/Status → detect faults → drive fan & buzzer → send to ESP32
ESP32
Init UART/Wi-Fi → receive data → connect MQTT broker → publish topics → dashboard auto-updates
DEVELOPMENT TOOLS
STM32CubeIDE
Firmware development & debugging for STM1/STM2
FreeRTOS
Priority-based task scheduling for real-time ops
Arduino IDE
ESP32 firmware — UART receive & MQTT publish
MQTT Dashboard
Live visualization of voltage, SOC, faults
SYSTEM OPTIMIZATION
Sensor validation & averaging • 100 ms periodic CAN transmission • Fault-priority handling • Temperature hysteresis for fan control
Real-Time EV Battery Management System with Safety Protections
8

## Slide 9
TESTING
Verification & Results
Every hardware module, communication link, and fault scenario was tested individually before full system integration.
Hardware
STM1 — sensor acquisition & CAN TX
STM2 — CAN RX & fault detection
INA219, NTC, MQ135 readings
Fan & buzzer driver circuits
Communication
CAN Bus: STM1 ↔ STM2 — verified
UART: STM2 ↔ ESP32 — verified
MQTT: ESP32 ↔ Dashboard — verified
I²C: STM1 ↔ INA219 — verified
Fault Scenarios
Under/Over-voltage — warning raised
Over-current — buzzer activated
High temperature — fan activated
Smoke / CAN failure — flagged
Real-Time EV Battery Management System with Safety Protections
9

## Slide 10
WRAP-UP
Conclusion & Future Scope
The Real-Time EV Battery Monitoring and Safety Protection System was successfully designed and implemented using dual STM32F407 controllers, CAN communication, and an MQTT-based IoT platform — reliably detecting abnormal conditions and enabling remote monitoring. This modular, scalable architecture provides a strong foundation for future Battery Management System (BMS) development.
FUTURE SCOPE
+
Cell balancing for improved battery life
+
State of Health (SOH) estimation
+
Coulomb Counting for accurate SOC
+
GPS integration for emergency tracking
+
Mobile app for instant notifications
+
Cloud analytics & ML-based fault prediction
Thank You
C-DAC ACTS, Pune | PGCP-DESD